# CprE 381: Computer Organization and Assembly-Level Programming

# Project Part 2 Report

Team Members:	__Camden Fergen__

__Emil Kosiac__

## Project Teams Group #:__TermProj1_1_02__

Refer to the highlighted language in the project 1 instruction for the context of the following questions.

# SW Pipeline

[1.a] Come up with a global list of the datapath values and control signals that are required during each pipeline stage.
In the above photo you can see all the required datapath and control signals that need to be passed and kept for every stage. Above each box, it also shows the number of signals going through each stage

[1.b.ii] high-level schematic drawing of the interconnection between components.

[1.c.i] include an annotated waveform in your writeup and provide a short discussion of result correctness.
This waveform (very confusing with the amount of signals) provides evidence of the functionality of the sw pipelined processor. At this specific time frame we can see the signal “s_RegWrData” with the value of 0x7D000001. This value, confirmed with the output value on Mars shows the current data value being written into $9. The most important part is that one of the registers used in the addi ($8) was written to in a previous instruction, thus demonstrating the successful use of the sw pipeline that we created. This also occurred towards the end of the program, but also to summaries without going into to much detail we can see that the rest of the tests passed without any data hazards or problems at all.

[1.c.ii] Include an annotated waveform in your writeup of two iterations or recursions of these programs executing correctly and provide a short discussion of result correctness. In your waveform and annotation, provide 3 different examples (at least one data-flow and one control-flow) of where you did not have to use the maximum number of NOPs.

[1.d] report the maximum frequency your software-scheduled pipelined processor can run at and determine what your critical path is (specify each module/entity/component that this path goes through).
The maximum frequency that the software scheduled pipeline was able to achieve was 47.88mhz, about twice as fast as the non pipelined processor. The critical path of this processor is as follows:
Imem → MipsReg → Zero unit (Just gets zero) → 32Bit Or gate → BranchOr (Determines if branching BE or BNE or neither) → Fetch unit (Jump reg mux) → PCReg

# HW Pipeline

[2.a.ii] Draw a simple schematic showing how you could implement stalling and flushing operations given an ideal N-bit register.

[2.a.iii] Create a testbench that instantiates all four of the registers in a single design. Show that values that are stored in the initial IF/ID register are available as expected four cycles later, and that new values can be inserted into the pipeline every single cycle. Most importantly, this testbench should also test that each pipeline register can be individually stalled or flushed.

[2.b.i] List which instructions produce values, and what signals (i.e., bus names) in the pipeline these correspond to.

[2.b.ii] List which of these same instructions consume values, and what signals in the pipeline these correspond to.

[2.b.iii] generalized list of potential data dependencies. From this generalized list, select those dependencies that can be forwarded (write down the corresponding pipeline stages that will be forwarding and receiving the data), and those dependencies that will require hazard stalls.

[2.b.iv] global list of the datapath values and control signals that are required during each pipeline stage

[2.c.i] list all instructions that may result in a non-sequential PC update and in which pipeline stage that update occurs.

[2.c.ii] For these instructions, list which stages need to be stalled and which stages need to be squashed/flushed relative to the stage each of these instructions is in.

[2.d] implement the hardware-scheduled pipeline using only structural VHDL. As with the previous processors that you have implemented, start with a high-level schematic drawing of the interconnection between components.

[2.e – i, ii, and iii] In your writeup, show the QuestaSim output for each of the following tests, and provide a discussion of result correctness. It may be helpful to also annotate the waveforms directly.

Base Tests:
We can see from the waveform that the data correctly lines up with the mars trace writing value 0x10010000 to register 0x01 which you can see at the cursor line. You can also notice from the waveform that the current instruction is stalling due to a data dependency with the next instruction is trying to write to the same RS reg, and then after that is cleared its causing the same stall in the memstage to finish writing back the value

Bubblesort:
From the waveform you see that the data lines up with the expected output from the mars trace of saving word address 1001004 and writing the value 0x0000000A near the 16460ns mark and then writing 0x000000000 to reg 0x10010000 the next cycle. You can also see that the branch unit is working which is correct as right before the save words as indicated by the branch unit signal.

CF Tests:
From this waveform we can see that in the next clock cycle starting 480ns it is correctly writing to the 0A reg which can be see from the mars.trace and matches the data being written of 0x0000001E. This proves the correctness of the program as the add instruction relies on the previous load instructions, and since its adding to the correct amount, the program is working as expected.

[2.e.i] Create a spreadsheet to track these cases and justify the coverage of your testing approach. Include this spreadsheet in your report as a table.

[2.e.ii] Create a spreadsheet to track these cases and justify the coverage of your testing approach. Include this spreadsheet in your report as a table.

[2.f] Report the maximum frequency your hardware-scheduled pipelined processor can run at and determine what your critical path is (specify each module/entity/component that this path goes through).
The maximum frequency achieved was 39.52mhz. This speed is slower than the software scheduled pipeline by about 8mhz. The critical path of this processor is as follows:
MipsReg → Inside of Reg for MipsReg → Subtractor (for getting 0) → RippleAdder Inside of Subtractor → Nbit mux inside of rippleAddr → OrGate inside of Nbit Mux → 32bit OrGate → Fetch unit jumpRegControl mux → PC reg